## Slide 1: Security Enhancement Of Openflow Networks

## Slide 2: Table of contents 01 04 02 05 03 06
Introduction
Objectives
Implementation
Reachability test
Server/Client and p2p Communication
Web service
07
Trace route
08
Future work

## Slide 3: Introduction 01

## Slide 4
With the increasing reliance on Software-Defined Networking (SDN) for its flexibility and programmability, the need for robust security mechanisms has become paramount. One of the major challenges facing SDN infrastructures is the susceptibility to Denial of Service (DoS) attacks.
When comparing Software-Defined Networking (SDN) with traditional networking approaches, several key differences emerge, impacting various aspects such as architecture, management, flexibility, scalability, and security.
So ,SDN is software-based, while traditional networking is hardware-based
Introduction

## Slide 5
Why SDN ?
Security:
Traditional Networking: Security mechanisms are typically distributed across network devices, making it challenging to enforce consistent policies and detect threats effectively. Security updates and patches may be device-specific and require manual intervention.
SDN: SDN offers improved security through centralized policy enforcement and granular visibility. Security policies can be defined and enforced centrally, with the controller dynamically adapting to mitigate security threats. Additionally, SDN facilitates integration with security tools and analytics platforms for enhanced threat detection and response.

## Slide 6: Objectives 02

## Slide 7
Deploy Initial SDN Network Configuration
Conduct Basic Connectivity Assessments
Implement server/client and p2p communication
Utilize Network Analysis Tools
Validate Routes Within the SDN Network
Fortify Infrastructure Against DoS Attacks
Develop Dynamic Mitigation Strategies

## Slide 8: Implementation 03

## Slide 9
Mininet and pox controller
OpenFlow and Python-based development
Open-Source and Customizability
Python-Based
Active Community and Documentation
Support for OpenFlow

## Slide 10: Why POX ?

## Slide 11: Mininet

## Slide 12: Our Topology
Our network architecture is characterized by a tree topology configuration. Within this framework, we have established two controllers operating on distinct ports, enhancing redundancy and fault tolerance within our network infrastructure.
Additionally, a core switch serves as the central node, facilitating efficient communication and traffic management among network components.
However, it is essential to recognize potential vulnerabilities inherent in this setup, particularly with regards to single points of failure and the implications thereof.

## Slide 13: Components selected for the design

## Slide 14: Implementing first topology
Command used for Mininet:
  $ sudo mn --switch ovsk --topo tree,depth=2,fanout=8 -- controller=remote,port=6100
Command used for pox:
  controllers 1(c0): $ ./pox.py openflow.of_01 --port=6100 forwarding.l2_pairs
This create : (1 pox controller – 9 OpenFlow switches – 64 pc device)

## Slide 15: Two modifications
2- Add second controller.
to work as a data backup or a data replication, because availability of a controller is essential to guarantee the availability of network services.
1- Reduce number of nodes in the network.
We decreased number of switches and hosts in the network to guarantee good performance

## Slide 16: Implementing second topology
Command used for Mininet:
  $ sudo mn --switch ovsk --topo tree,depth=2,fanout=4 --controller remote,port=6100 --controller remote,port=6101
Commands used for pox:
  controllers 1(c0): $ ./pox.py openflow.of_01 --port=6100 forwarding.l2_pairs
  controllers 2(c1): $ ./pox.py openflow.of_01 --port=6101 forwarding.l2_pairs
This create : (2 pox controller – 5 OpenFlow switches – 16 pc device)

## Slide 17: Creating the network

## Slide 18: Controllers is up
C0 is up
C1 is up

## Slide 19
Nodes
Links

## Slide 20: Tree topology

## Slide 21: Reachability test 04

## Slide 22: Ping command

## Slide 23: Flow rules
S2 flow rules after h1 ping on h2
S1 flow rules after pingall and there is more flow rules

## Slide 24: Server/Client Communication 05.1

## Slide 25: Server/Client Communication
It is a software solution used for transferring files across the internet using ftp protocol.
Wing FTP Server Admin
This server can do multiple things like
File Access
Server logs
Audit & Report
Graphs & activity
Overview

## Slide 26: NAT Protocol
Running the nat protocol on network to make the hosts go online by giving them public ip addresses.
Also to communicate with the ftp server.
Ping on google’s DNS:

## Slide 27: NAT Protocol
As we see all interfaces are defined on the nat0.
Also have an ip address 10.0.0.17

## Slide 28: Configurations of the server
First ,create a domain and asigen an ip address to it.
Select the services.

## Slide 29: Configurations of the server
Secondly ,adding users ( submit the credentials ).
Select the directory of the files.

## Slide 30: Configurations of the server
Select the file and directory access (assigning privileges).

## Slide 31: Configurations of the server
Edit the user directory to the desired folder which contains the files of the server.

## Slide 32: Configurations of the server
Finally, the domain is online.

## Slide 33: Configurations of the server
Adding some privileges on some files.

## Slide 34: On SDN Network
From the CLI of h1.
Connect to the server by ip address.
Enter the credentials (username,password).
Ls command to see the files on the server.
Get (download)some files from the server.
Try to download the banned file.
1
2
3
4
5
6
7
8

## Slide 35: On SDN Network
Also if we want to upload some files to the server.

## Slide 36: Capturing the packets using WireShark
TCP uses a three-way handshake to establish a reliable connection and Authentication between the host and the server.
After that the process of transferring files starts using ftp protocol.

## Slide 37: Capturing the packets using WireShark
If we follow the tcp stream we’ll see all the data (traffic) as a plaintext because ftp protocol is not secure.

## Slide 38: Logs & Status
Domain log saved in the server.
Also all sessions.
Ex: the last uploaded files to the server.

## Slide 39: Logs & Status
Audit & Reports also saved in the server.
Includes (ID,protocol,Action,username,time,file name,size and server ip address)

## Slide 40: Logs & Status
Graphs shows the number of online sessions ,the download and upload speed.

## Slide 41: Peer To Peer Communication 05.2

## Slide 42: Peer To Peer Communication
Both peers exchange information with each other without the need for any intermediate servers.
p2p
Nc is a powerful and versatile networking utility tool used for reading from and writing to network connections.
It provides a simple and straightforward way to create TCP/IP connections, listen for incoming connections, transfer data, and perform various network-related tasks.
Netcat tool

## Slide 43
h1 is listening for an incoming connections
h16 send the file

## Slide 44: wireshark
The start of the connection

## Slide 45: wireshark
The end of the connection and file transferred successfully

## Slide 46: Web service 06

## Slide 47: HTTP Server
What is http server ?
Implementation of http server

## Slide 48: HTTP Server
Access the http server from another host
Let’s breakdown the command
Wget http://10.0.1.1:8000/p.html

## Slide 49: HTTP Server
Packet capture :
Notice the first 3 packets

## Slide 50: HTTP Server
Packet capture
Notice the last 3 packets

## Slide 51: traceroute 07

## Slide 52: traceroute
What is traceroute ? why we use traceroute ?
Installation of traceroute

## Slide 53: traceroute
Problem faced

## Slide 54: traceroute
How we solve the problem ?

## Slide 55: traceroute
Tool usage

## Slide 56
Route validation
1)What is the meaning of route validation ?
2)What are attributes and Techniques used to validate open flow packets through network?
3)Verify best path (route ) through network?

## Slide 57: Bandwidth
Bandwidth utilization refers to the amount of network capacity being consumed by traffic flows on specific routes or links within the network. Monitoring bandwidth utilization helps in ensuring that.
Bw=total data transferred (inbits)/capture duration
We need First to add links between End switches
py net.addLink(s2,s3)
py net.addLink(s3,s4)
py net.addLink(s4,s5)

## Slide 58: capturing Using Wireshark.
What we observed repeating the test through different Destinations?
Why Should we Customize our network ?
s2-eth1<->h1-eth0…bw=98*8*8bits/(32-29)sec
s1-eth1<->s2-eth5…bw=98*8*8bits/(22-19)sec
s1-eth2<->s3-eth5…bw=98*8*8bits/(27-24)sec

## Slide 59: Future work 08

## Slide 60: Work in progress : DOS Attack
Customize network to achieve SOP ( Singlepoint of fauilre concept)?
What is DOS attack ? what is DDOS attack ?
how could it be done ?

## Slide 61: THANKS !