## Slide 1
Security Enhancement Of Openflow Networks
Supervised by Prof. Dr. Ihab Abdelwahab Ali
By
Eng. Khaled Elsayed Ahmed

## Slide 2
Project vision and mission
01.
02.
03.
Proactive Detection and Prevention
To develop and implement advanced, real-time monitoring and detection mechanisms within SDN networks that can identify and mitigate potential DoS attacks before they can impact network performance and security.
To conduct cutting-edge research into new methodologies and technologies for securing SDN networks, ensuring that our solutions evolve with the changing landscape of cyber threats and remain at the forefront of DoS defense strategies.
To foster partnerships with academic institutions, industry leaders, and cybersecurity experts to share knowledge, develop best practices, and educate network administrators on the latest security protocols and techniques to protect SDN networks from DoS attacks.
To develop and implement advanced security protocols and mechanisms within SDN architectures that proactively detect, prevent, and respond to DoS attacks. Our mission is to enhance the robustness and reliability of SDN networks through continuous research, innovation, and collaboration with industry leaders, fostering a safer digital esystem.

## Slide 3
SECURITY ENHANCEMENT OF OPENFLOW NETWORKS
PHASE 1
phase 1
phase 2
phase 3
phase 4
Implementation of SDN topology
Adding services to Network
DOS Attack simulation and Detection
Mitigation from DOS attack

## Slide 4
PHASE 1
IMPLEMENTATION
A DEEP UNDERSTANDING OF SDN NETWORKS AND THEIR IMPLEMENTATION

## Slide 5
SDN
1)SDN Definition.
2)SDN Architecture.
3)SDN benefits.
IMPLEMENTATION

## Slide 6
1)NFV (NETWORK FUNCTIONS VIRTUALIZATION)
2)HOW OPENFLOW HELPS IN SDN NETWORKS:
3)WHAT IS OPEN VSWITCH?
SDN Architecture
IMPLEMENTATION

## Slide 7
IMPLEMENTATION
Implementation with Mininet and POX Controller
Why we use Pox controller ?
1)Flexibility and Customizability
2)Active Community and Documentation
3)Support for SDN Concepts
Mininet&pox

## Slide 8
IMPLEMENTATION
Setting the Stage for SDN Exploration
1)Installing ubuntu
2)Installing Mininet and pox controller
$. /pox.py openflow. of_01 --port=6100 forwarding. l2_pairs
$. /pox.py openflow. of_01 --port=6101 forwarding. l2_pairs
$sudo mn --switch ovsk --topo tree,depth=2,fanout=4--
controller=remote,ip=127.0.0.1,port=6100
,
Mininet&pox

## Slide 9
Testing Network Connectivity
IMPLEMENTATION
1)A ping from h1 to h2 (send 4 packets)
2)S1 flow rules after pingall and there are more flow rules.

## Slide 10
PHASE 2
SERVICES
ENHANCEMENT OF SDN COMMUNICATION SERVICES BY APPLYING DIFFERENT STRATEGIES

## Slide 11
SERVICES
SERVER TO CLIENT COMMUNICATION
WING FTP SERVER ADMIN
IT IS A SOFTWARE SOLUTION USED FOR TRANSFERRING FILES ACROSS THE INTERNET USING FTP PROTOCOL.
THIS SERVER CAN DO MULTIPLE THINGS LIKE
FILE ACCESS
SERVER LOGS
AUDIT & REPORT
GRAPHS & ACTIVITY

## Slide 12
SERVICES
CONFIGURATION OF THE SERVER
CREATION OF THE FTP SERVER

## Slide 13
SERVICES
ON SDN NETWORK
FROM THE CLI OF H1.
CONNECT TO THE SERVER BY IP ADDRESS.
ENTER THE CREDENTIALS (USERNAME,PASSWORD).
LS COMMAND TO SEE THE FILES ON THE SERVER.
GET (DOWNLOAD)SOME FILES FROM THE SERVER.
TRY TO DOWNLOAD THE BANNED FILE.

## Slide 14
SERVICES
ON SDN NETWORK
ALSO IF WE WANT TO UPLOAD SOME FILES TO THE SERVER.

## Slide 15
SERVICES
PEER TO PEER COMMUNICATION
BOTH PEERS EXCHANGE INFORMATION WITH EACH OTHER WITHOUT THE NEED FOR ANY INTERMEDIATE SERVERS.
NC IS A POWERFUL AND VERSATILE NETWORKING UTILITY TOOL USED FOR READING FROM AND WRITING TO NETWORK CONNECTIONS.
IT PROVIDES A SIMPLE AND STRAIGHTFORWARD WAY TO CREATE TCP/IP CONNECTIONS, LISTEN FOR INCOMING CONNECTIONS, TRANSFER DATA, AND PERFORM VARIOUS NETWORK-RELATED TASKS.

## Slide 16
SERVICES
NETCAT
H1 IS LISTENING FOR AN INCOMING CONNECTION
H16 SENDS THE FILE

## Slide 17
SERVICES
WEB SERVICE
IMPLEMENTATION OF HTTP SERVER
THE HOST CAN SERVE WEB CONTENT AND RESPOND TO HTTP REQUESTS FROM OTHER HOSTS IN THE NETWORK.

## Slide 18
SERVICES
WEB SERVICE
ACCESS THE HTTP SERVER FROM ANOTHER HOST
LET’S BREAKDOWN THE COMMAND
Wget http://10.0.1.1:8000/p.html

## Slide 19
SERVICES
TRACEROUTE
INSTALLATION OF TRACEROUTE

## Slide 20
SERVICES
TRACEROUTE
PROBLEM FACED

## Slide 21
SERVICES
TRACEROUTE
HOW WE SOLVE THE PROBLEM ?

## Slide 22
SERVICES
TRACEROUTE
TOOL USAGE

## Slide 23
SERVICES
THE LAST UPDATED TOPOLOGY WITH PYTHON SCRIPT

## Slide 24
SERVICES
THE PYTHON SCRIPT THAT USED TO CREATE THE TOPOLOGY

## Slide 25
PHASE 3
DOS ATTACK SCENARIO
DOS ATTACK AND DETECTION

## Slide 26
THE CYBER KILL CHAIN MODEL
  Developed by Lockheed Martin
  It is part of the Intelligence Driven Defense model for identification and prevention of cyber intrusions activity.
  The model identifies what the adversaries must complete in order to achieve their objective.
The seven steps of the Cyber Kill Chain enhance visibility into an attack and enrich an analyst’s understanding of an adversary’s tactics, techniques and procedures.
DOS ATTACK SCENARIO

## Slide 27
RECONNAISSANCE
  Goal: Gather information about the target.
  Action: Perform network scanning to identify open ports and services running on h1 (HTTP server).
  Details: Using nmap on h1 to discover open port 8080, which indicates the HTTP server is running.
DOS ATTACK SCENARIO
1-ARP Packets:h16 will need to resolve the IP addresses of other hosts (like h1) to their MAC addresses. This triggers ARP requests and replies.
2-TCP Packets:h16 sends TCP/IP packets to the specified IP range and listens for responses to determine which hosts are active and which ports are open

## Slide 28
  Goal: Create a deliverable payload for the attack.
  Action: Prepare the DoS attack payload using hping3.
  Command: $ hping3 -d 300 -S -w 64 -p 8080 --flood --rand-source -V 10.0.0.1
WEAPONIZATION
DOS ATTACK SCENARIO
1-Payload: Overwhelms h1 by sending a high volume of SYN packets to port 8080.
2-Flood Mode: Maximizes impact by sending packets rapidly.
3-Random Source IPs: Evades detection and filtering by the target.
4-Data Size: Each packet includes 300 bytes of data, adding to the target's load.
5-Verbose Output: Offers detailed feedback for monitoring and analysis.

## Slide 29
  Goal: Deliver the weapon to the target environment.
  Action: Initiate the DoS attack from h16.
  Details: Use hping3 to send a high volume of TCP packets to port 8080 on h1.
DELIVERY
DOS ATTACK SCENARIO
  When running the command of the attack on h16 ,the server flooded with tcp packets from random ip addresses.

## Slide 30
DETECTION AND CAPTURE OF THE ATTACK
Wireshark
TCPDUMP
FlowRules

## Slide 31
  Goal: Trigger the payload on the target system.
  Action: Exploit the target by overwhelming its resources.
  Details: The high volume of TCP packets causes h1 to become unresponsive.
  Impact:
EXPLOITATION
DOS ATTACK SCENARIO
1.Resource Exhaustion: CPU, memory, and network bandwidth on h1 are consumed by the attack, causing a denial of service.
2.Service Unavailability: The HTTP server on h1 becomes unresponsive to legitimate requests.
1.Wireshark: Capture and analyze the flood of SYN packets and the lack of responses from h1 as before.
2.Ping Test: Observe timeouts when pinging h1 from another host (h10), confirming the DoS impact.
VERIFICATION
  All packets are lost this mean that the impact of the attack is obvious where h10 does not receive any replay from h1 because of the attack on it.

## Slide 32
  Goal: Establish command and control channels to communicate with the compromised system.
COMMAND AND CONTROL (C2)
DOS ATTACK SCENARIO
  For a DoS attack, this stage may not apply as there is no need for a C2 channel in a simple DoS scenario.
INSTALLATION
  Goal: Install a backdoor or other persistent access mechanism.
  For a DoS attack, this stage does not apply since the goal is disruption rather than persistent access.

## Slide 33
  Goal: Achieve the attacker’s goals. which is Disrupt the availability of the HTTP server by overwhelming it with requests, making it unable to respond to legitimate traffic.
  Action: Disrupt service on h1(http server).
  Details: Monitor the effectiveness of the DoS attack by pinging h1 from h10 to verify that packets are dropped as we see before
ACTIONS ON OBJECTIVES
DOS ATTACK SCENARIO

## Slide 34
SOME NOTES WHEN APPLYING THE KILL CHAIN MODEL IN THE SDN NETWORK USING DOS
During Attack:
    Multiple OpenvSwitches go down due to resource exhaustion.
    Network segments connected through these switches become temporarily disconnected.
Post-Attack:
    The switches recover and re-establish connections.
    Network functionality is restored without manual intervention.

## Slide 35
PHASE 4
MITIGATION
MITIGATION FROM DOS ATTACK

## Slide 36
siem solution.
PRACTICAL DETECTION
MITIGATION
eg:
  IBM Qradar
  Splunk

## Slide 37
PROBLEM OVERVIEW
Wireshark
TCPDUMP
FlowRules

## Slide 38
PROBLEM OVERVIEW
Crucial effect of DOS attack on enterprises.
MITIGATION
  availability concept
  financial issues
  Negative media attention
  launching other attacks

## Slide 39
limitations of traditional DoS mitigation techniques .
e.g:
MITIGATION
TRADITIONAL MITIGATION TECHNIQUES
  static filtering
  resource limitations
  Challenge-Response Systems (solving a captcha)

## Slide 40
MITIGATION PRINCIPLES
MITIGATION
implementing a python script based on :
  rate limiting ( with defining a threeshold )
  subnet checking

## Slide 41
MITIGATION
MITIGATION
planting the python script inside pox , ext directory

## Slide 42
SCRIPT OVERVIEW
MITIGATION
  Imports and Logger Setup
  Threshold and Tracking Variables

## Slide 43
SCRIPT OVERVIEW
MITIGATION
  subnet checking function
  packet dropping function

## Slide 44
SCRIPT OVERVIEW
MITIGATION
  rate limiter function
  Launch Function

## Slide 45
LAUNCHING SYSTEM
  running mitigation script in controllers .
  doing the same with the other controller, but with changing port .
MITIGATION

## Slide 46
DETECTION
MITIGATION
controller outputs

## Slide 47
DETECTION
MITIGATION
Detection using flow tables
focus on the added last section , actions .

## Slide 48
DETECTION
MITIGATION
  testing reachability immediately after applying mitigation script .
Detection using ping

## Slide 49
DETECTION
MITIGATION
  testing reachability after few seconds .
  0% packet loss and high data rates as required .
Detection using ping

## Slide 50
FUTURE WORK
- MACHINE LEARNING-BASED ANOMALY DETECTION
- GEO-FENCING AND TRAFFIC FILTERING BASED ON LOCATION
FUTURE WORK